## Slide 1
Image Challenge
An 80-year-old woman was admitted to the intensive care unit with severe second- and third-degree burns. On laboratory studies, she was noted to have a platelet count of 930,000 per cubic millimeter. Manual analysis of a subsequent peripheral-blood smear identified a platelet count of 115,000 per cubic millimeter. What is the cause for this discrepancy?
1. Pseudothrombocytopenia due to giant platelets
2. Pseudothrombocytopenia due to plate clumping associated with EDTA
3. Pseudothrombocytosis due to cryoglobulin-related interference by cryoprecipitates
4. Pseudothrombocytosis due to presence of microorganisms
5. Pseudothrombocytosis due to red cell fragments
Q:

## Slide 2
Answer:
Image Challenge
An 80-year-old woman was admitted to the intensive care unit with severe second- and third-degree burns. On laboratory studies, she was noted to have a platelet count of 930,000 per cubic millimeter. Manual analysis of a subsequent peripheral-blood smear identified a platelet count of 115,000 per cubic millimeter. What is the cause for this discrepancy?
Q:
Pseudothrombocytosis due to red cell fragments
The correct answer is pseudothrombocytosis due to red cell fragments. In patients with severe burn injuries, heat-induced disruption of the red-cell membranes can generate smaller cells that may be incorrectly counted as platelets by automated counters.